## Slide 1: Chapter 6
Functions

## Slide 2: Objectives
Deconstruct function implementations
Compare function calling conventions
Manipulate stack memory
Create functions in Assembly

## Slide 3: Web Resources
Wikis
https://en.wikipedia.org/wiki/Calling_convention
https://en.wikipedia.org/wiki/X86_calling_conventions
https://en.wikibooks.org/wiki/X86_Disassembly/Calling_Conventions
https://wiki.osdev.org/Calling_Conventions
Developer
https://developer.apple.com/library/archive/documentation/DeveloperTools/Conceptual/LowLevelABI/000-Introduction/introduction.html#/apple_ref/doc/uid/TP40002521 (OS X ABI Function Call Guide)
https://docs.microsoft.com/en-us/cpp/cpp/calling-conventions (x86 Calling Conventions)
https://docs.microsoft.com/en-us/cpp/build/x64-calling-convention (x64 Calling Convention)
https://refspecs.linuxfoundation.org/elf/x86_64-abi-0.99.pdf (AMD64 ABI)
https://www.agner.org/optimize/calling_conventions.pdf (Calling Conventions)

## Slide 4: Stack Memory Primer
Stack grows and shrinks as functions are called and return.
Stack grows and shrinks as local variables are created (pushed) and dereferenced (popped).
Stack has an OS-dependent size limit per process/thread.
Every function call, including main() and recursive calls, has a stack frame.
A stack frame is used to store a function’s local variables.
Stack memory grows down, with addresses descending.
Every memory slot holds 4 bytes in 32-bit mode or 8 bytes in 64-bit mode.
Values are stored by default in Little-Endian form.
In x86_64, all functions must be 16-byte aligned.

## Slide 5: Caller and callee

## Slide 6: x86_64 Calling Conventions
Parameters are passed in left to right order up to the maximum registers supported. Any remaining parameters are passed in reverse order from right to left via the stack
Some registers are caller-saved (volatile), while others are callee-saved (non-volatile). Consequently, if you want to save caller-saved register values, you need to do so in the calling function because they will likely be overwritten during function execution (e.g., rax).
rax is used as the return register in most cases, while x/y/zmm0 is used for a floating-point return.
The caller is responsible for cleaning up stack

## Slide 7: x86_64 Calling Conventions

## Slide 8: Program 6.1 – Sum in x86_64

## Slide 9: Pass-by-reference

## Slide 10: Before parameters are passed (Figure 6.1)

## Slide 11: After CALL instruction (Figure 6.2)

## Slide 12: After establishing frame and saving rbx (Figure 6.3)

## Slide 13: After RET instruction (Figure 6.4)

## Slide 14: Parameter passing in MS x64

## Slide 15: Stack alignment
Required in 32-bit macOS
Required in 64-bit for all platforms
Methods include using NOP, subtracting from rsp, using AND, and using compiler flags

## Slide 16: Microsoft x64 shadow space

## Slide 17: x86_64 Sum disassembly (MASM)

## Slide 18: x86 Calling Conventions – cdecl
Parameters are passed in reverse order (right to left) via the stack
eax, ecx, and edx are caller-saved (volatile), while the rest of the general purpose registers are callee-saved (non-volatile)
eax is used as the return register in most cases and st(0) is used for a floating-point return
The caller is responsible for cleaning up stack

## Slide 19: Visual Studio Calling Convention Settings

## Slide 20: x86 Calling Conventions – stdcall
Parameters are passed in reverse order (right to left) via the stack
eax, ecx, and edx are caller-saved (volatile), while the rest of the general purpose registers are callee-saved (non-volatile)
eax is used as the return register in most cases and st(0) is used for a floating-point return
The callee is responsible for cleaning up stack

## Slide 21: Some useful details
If the Floating-Point Unit (FPU) stack is used, it must be clear upon entry into a function and upon exit, except for st(0), which may be holding the return value. The FPU is discussed in Chapter 8.
In 32-bit, addresses for pass-by-reference are passed on the stack. Registers serve as an intermediary to obtain the parameter address at run-time using the LEA instruction, which is then moved or pushed to the stack.
lea -0x8(%ebp), %eax # a parameter address is loaded into eax
mov %eax, (%esp) # address copied to where esp is pointing
In 64-bit, the address can be moved directly to a register for pass-by-reference.
lea -0x8(%rbp), %rdi # a parameter address is loaded into rdi
In 64-bit, if using varargs functions such as printf(), the al register, which is the low 8 bits of rax, is used to store the number of SSE registers used.
Refer to the Web resources for further detail on calling conventions. In particular, the reference by Agner Fog (https://www.agner.org/optimize/calling_conventions.pdf) and the application binary interface (ABI) documents such as https://refspecs.linuxfoundation.org/elf/x86_64-abi-0.99.pdf are the most useful in terms of comparing calling conventions and providing detailed overviews.

## Slide 22: Program 6.2 – Sum in C++

## Slide 23: Sum main() disassembly

## Slide 24: Sum sum() disassembly

## Slide 25: Sum stdcall versus fastcall

## Slide 26: Chapter 6 Key Terms
application binary interface (ABI)
callee
caller
calling conventions
cdecl
epilogue
fastcall
functions
leaf functions
Little-Endian
Microsoft x64
procedures
prologue
red zone
shadow (home) space
stack frame
stack memory
stdcall
Streaming SIMD Extentions (SSE)
System V AMD64 (AMD64)